## Slide 1
Backend-Dependent Stability on Legacy HBM GPUs
ROCm/HIP vs Vulkan on Vega/gfx900: residual paths, offload-layer semantics, and reproducible diagnosis
Akira Ito | AETS (Akatsuki Enterprise Technology Solutions) | aets-giken@hiroshima-aktk.com
IEICE GNW-68 | Kyushu Sangyo University | March 9, 2026
1
Background & Motivation
Official support matrices not listed gfx900 in ROCm 7.2, but real systems can still execute through residual code and artifact paths.
For students and small labs, the key question is whether execution is possible, stable, and reproducible.
We built a matched dual-backend testbed on the same Vega device to separate support policy, backend choice, and runtime behavior.
Goal: explain why "unsupported" and "unusable" are not the same statement.
2
Problem Statement
Legacy Vega GPUs are often treated as categorically unsuitable for modern ROCm workloads.
Success or failure may be decided at different layers: distribution presets, build targets, init validation, backend macros, or runtime compute paths.
We ask: is instability caused by Vega itself, or by a specific backend path under matched conditions?
3
Confirmed Facts from Investigation
A. gfx900 Gate Matrix (repo: work_log/investigations/gfx900_gate_matrix.md)
Layer | Current handling of gfx900 | Blocks / Allows
Official matrix (ROCm 7.2) | gfx900 not listed in GPU target list | Blocks (official scope)
CMake filter (ollama) | Default regex excludes gfx900; manual override possible via AMDGPU_TARGETS | Blocks default / Allows manual
rocBLAS artifacts | Kernels.so-000-gfx900.hsaco found in /usr/lib/ollama/rocblas/library/ | Allows
Runner init validation | Deep init probe (GGML_CUDA_INIT=1): gfx900 recognized as valid agent | Allows
Source macros (hip.h, common.cuh) | __gfx900__ → GCN5 classification retained; dp4a path exists | Allows
Runtime execution | ROCm/HIP: all num_gpu values OK. Vulkan: SIGSEGV when num_gpu>=1 | Backend- dependent
B. num_gpu Semantics Trace (repo: work_log/investigations/numgpu_semantics_trace.md)
Stage | Code location | Meaning
Python client | ollama-python/_types.py:109 | Load-time option
Ollama CLI | cmd/interactive.go:112 | "number of layers sent to GPU"
Server assign | llm/server.go:992,1063 | requestedLayers = NumGPU
Runner bridge | llama/llama.go:266 | cparams.n_gpu_layers
llama.cpp | include/llama.h:289 | "layers stored in VRAM"
Conclusion: num_gpu is offloaded layer count, NOT GPU device count. num_gpu>=2 does not imply multi-GPU.
C. Related Literature (cited, not reproduced in this repo)
LLNL differential testing (arXiv:2410.09172): 600K+ auto-generated kernels showed FP32 divergence ~9% between NVIDIA V100 and AMD MI250. Root causes: vendor-specific math libraries, compiler flags, HIPIFY artifacts. Motivates our backend-aware validation approach.
gem5 Vega modeling (Univ. Wisconsin-Madison): GPUFS mode runs real Linux kernel + unmodified amdkfd driver. Validated against physical Vega 56 with avg 6% error. Establishes Vega as academically credible.
ROCm SDMA workarounds (AMD docs + LUMI reports): HSA_ENABLE_SDMA=0 bypasses faulty DMA with Blit kernel fallback (~80% bandwidth). HSA_OVERRIDE_GFX_VERSION enables unsupported GPU execution — the override used in our experiments.
These are external references. All claims in this poster are based solely on repo-internal evidence (Sections 3A, 3B, 6).
4
Engineering Challenges
gfx900 excluded by official matrices and default build filters, yet residual code and artifacts still retain gfx900 handling.
`num_gpu` is easily misread as GPU count; our code trace confirms it means offloaded layers.
The same Vega GPU can succeed on ROCm/HIP and fail on Vulkan under the same model and prompt.
Diagnosis must be layer-by-layer and evidence-driven, not reduced to "legacy GPU bad".
5
Evidence-First Investigation Strategy
Investigation Layers
Layer | Intervention | Effect
L1: Distribution / Build | Inspect support matrix, presets, target filters, installed artifacts | Locate where gfx900 is blocked, allowed, or only partially retained
L2: API Semantics | Trace num_gpu through client → server → runner → llama.cpp | Fix interpretation: offloaded layers, not GPU count
L3: Runtime Comparison | Run matched ROCm (:11435) and Vulkan (:11434) tests | Isolate backend-specific failure modes on identical hardware
L4: Evidence Capture | Structured work logs, journal traces, backend probes, rocm-smi, ollama ps | Localize crashes and make claims reproducible
Approach prioritizes falsifiable diagnosis and reproducibility over optimistic one-off success.
6
Experimental Results
Test Environment
Component | Specification
GPU | AMD Radeon RX Vega 56 (gfx900), 8 GB HBM2
OS / Kernel | EndeavourOS, Kernel 6.18.16-1-lts
ROCm path | Ollama 0.17.5 via :11435, library=ROCm, libggml-hip.so
Vulkan path | Ollama 0.17.4 via :11434, library=Vulkan, same model/prompt
Override | HSA_OVERRIDE_GFX_VERSION=9.0.0 (ROCm service only)
Note | Vulkan=0.17.4 vs ROCm=0.17.5: version difference is inherent to the dual-install; both tested as-shipped
Matched-Condition Results (qwen3.5:2b, NUM_PREDICT=512)
num_gpu | ROCm (:11435) run_20260307_012643 | Vulkan (:11434) run_20260307_013050
0 (CPU only) | OK (46.7s, eval_count=512) | OK
1 | OK (48.7s, eval_count=512) | FAIL (HTTP 500, SIGSEGV)
2 | OK (47.7s, eval_count=512) | FAIL (HTTP 500, SIGSEGV)
-1 (all layers) | OK (44.3s, eval_count=512) | FAIL (HTTP 500, SIGSEGV)
Note: Vulkan succeeded with num_gpu=0 (no GPU offload). Failures occurred only when num_gpu>=1 (GPU compute path active). ROCm results are within this tested scope (single model, short fixed runs); broader workloads may differ. Model dependency observed: tinyllama succeeded on Vulkan in earlier tests (run_20260307_003423, 20/20 OK); qwen3.5:2b triggers the SIGSEGV. Also: num_gpu=0 runs may produce eval_count=512 with response_chars=0 — this is a model output quirk, not a crash.
Crash localization: Vulkan SIGSEGV occurred in ggml_backend_sched_graph_compute_async → computeBatch, after model load completed and runner started. This is a compute-phase failure, not an initialization failure.
Failure Diagnosis
Hypothesis | Expected Evidence | Observed
Vega is generally unusable | Both backends fail on same GPU | Contradicted: ROCm/HIP succeeded
num_gpu means GPU count | Failure implies multi-GPU entry | Contradicted: code trace = offloaded layers
Vulkan compute-path instability | Load OK; crash after runner start in compute stack | MATCH
Why gfx900 Still Works Sometimes
ROCm changelog says "no longer built by default" rather than "forbidden." In the local install, gfx900 hsaco artifacts and libggml-hip.so strings were verified present.
Interpretation:
unsupported = unguaranteed and untested, not necessarily impossible.
Limitations & Future Work
Limitations: Matched comparison used short fixed runs (1 epoch, 512 tokens) with a single model (qwen3.5:2b). Vulkan and ROCm Ollama versions differ (0.17.4 vs 0.17.5). tinyllama behaved differently from qwen3.5 on Vulkan, indicating model-dependent failure conditions. Results should not be generalized beyond this tested scope without further verification.
Future work:
Multi-epoch stress tests, additional models (llm-jp, phi-3), ROCm version comparison (6.x vs 7.x), and GGML_CUDA_NO_PEER_COPY experiments to isolate offload-path failure mechanisms. Reproducibility infrastructure (workaround matrix with 15 documented cases) is available in the repo for community use.
7
Takeaway & Key Messages
✅
Support Status ≠ Execution Reality
Official exclusion does not imply impossibility. Gate matrix shows 5 of 6 layers allow gfx900 execution. Residual code paths and shipped artifacts make partial execution possible.
💡
Backend Choice Dominates
On the same Vega device with qwen3.5:2b, ROCm/HIP passed all num_gpu conditions within tested scope. Vulkan failed when num_gpu>=1 (GPU offload active). Failure is backend-specific, not architecture-wide. Model dependency (tinyllama vs qwen) exists.
🔬
Reproducibility Before Claims
All claims backed by specific run_ids and code traces. Key runs: run_20260307_012643 (ROCm qwen), run_20260307_013050 (Vulkan qwen), run_20260307_003423 (tinyllama 20/20 OK). Gate matrix and workaround matrix (15 cases) in repo.
Unsupported ≠ Impossible. | Legacy ≠ Poor. | Backend choice matters.