## Slide 1
Backend-Dependent Stability on Legacy HBM GPUs
ROCm/HIP vs Vulkan on Vega/gfx900: residual paths, offload-layer semantics, and reproducible diagnosis
Akira Ito | AETS (Akatsuki Enterprise Technology Solutions) | aets-giken@hiroshima-aktk.com
IEICE GNW-68 | Kyushu Sangyo University | March 9, 2026
1
Background & Motivation
Official support matrices exclude gfx900 in ROCm 7.2, but real systems can still execute through residual code and artifact paths.
For students and small labs, the key question is whether execution is possible, stable, and reproducible.
We built a matched dual-backend testbed on the same Vega device to separate support policy, backend choice, and runtime behavior.
Goal: explain why "unsupported" and "unusable" are not the same statement.
2
Problem Statement
Legacy Vega GPUs are often treated as categorically unsuitable for modern ROCm workloads.
Success or failure may be decided at different layers: distribution presets, build targets, init validation, backend macros, or runtime compute paths.
We ask: is instability caused by Vega itself, or by a specific backend path under matched conditions?
3
Related Work
A. Numerical Divergence (LLNL, arXiv:2410.09172)
Small self-contained tests expose cross-platform numeric differences.
Chart: NVIDIA vs AMD Numerical Divergence Rate (%)
| FP32 Direct | FP64 Direct | FP64 HIPIFY
Divergence Rate | 9 | 0.98 | 1.1
Key insight: Compilation success does not guarantee equivalent behavior. This motivates backend-aware validation.
B. gem5 Vega Modeling (Univ. of Wisconsin-Madison)
SE mode → GPUFS mode: real Linux kernel + unmodified amdkfd driver
Chart: gem5 vs Physical Vega 56: Simulation Error (%)
| Speedup (avg) | Speedup (worst) | Instr Count (avg) | Instr Count (worst)
Error (%) | 6 | 10 | 6 | 7
Vega architecture is well-characterized in academic simulation, establishing credibility as a research platform.
C. Support Matrices vs Residual Paths
Layer | Observation | Implication
ROCm 7.2 matrix | gfx900 not listed, not officially guaranteed | Support status alone does not decide runtime possibility
Source / artifacts | __gfx900__ paths, hsaco artifacts, HIP library strings remain | Residual paths can still enable partial execution
4
Engineering Challenges
gfx900 is excluded by current official support matrices and default build filters, yet some code and artifacts still retain gfx900 handling.
`num_gpu` is easily misread as GPU count; code tracing shows it actually means offloaded layers.
The same Vega GPU can succeed on ROCm/HIP and fail on Vulkan under the same model and prompt.
Diagnosis must be layer-by-layer and evidence-driven, not reduced to "legacy GPU bad".
5
Evidence-First Investigation Strategy
Investigation Layers
Layer | Intervention | Effect
L1: Distribution / Build | Inspect support matrix, presets, target filters, installed artifacts | Locate where gfx900 is blocked, allowed, or only partially retained
L2: API Semantics | Trace `num_gpu` through client → server → runner → llama.cpp | Fix interpretation: offloaded layers, not GPU count
L3: Runtime Comparison | Run matched ROCm (:11435) and Vulkan (:11434) tests | Isolate backend-specific failure modes on identical hardware
L4: Evidence Capture | Structured work logs, journal traces, backend probes, rocm-smi, ollama ps | Localize crashes and make claims reproducible
Approach prioritizes falsifiable diagnosis and reproducibility over optimistic one-off success.
6
Experimental Results
Test Environment
Component | Specification
GPU | AMD Radeon RX Vega 56 (gfx900), 8 GB HBM2
OS / Kernel | EndeavourOS, Kernel 6.12.74-1-lts
ROCm path | Ollama 0.17.5 via :11435, library=ROCm, libggml-hip.so
Vulkan path | Ollama 0.17.4 via :11434, library=Vulkan, same model/prompt
Matched-Condition Verification Results
Stage | Verification | Evidence | Status
1. Support Gate Check | Matrix / preset / artifact review | gfx900 excluded from official matrix, but residual code and artifacts remain | OK
2. API Semantics | `num_gpu` meaning trace | client → server → llama.cpp shows offloaded layers, not GPU count | OK
3. ROCm/HIP Run | qwen3.5:2b, num_gpu=0,1,2,-1 | All conditions succeeded under matched conditions (46-49s each) | OK
4. Vulkan Run | Same model and parameters | num_gpu=0 ok; num_gpu>=1 returned HTTP 500 (SIGSEGV) | FAIL
5. Crash Localization | journal / stack trace | Load completed; SIGSEGV in computeBatch after runner start | FAIL (Vulkan)
Failure Diagnosis
Hypothesis | Expected Evidence | Observed
Vega is generally unusable | Both backends should fail on the same GPU | Contradicted by ROCm/HIP success
`num_gpu` means GPU count | Failure should imply multi-GPU entry | Contradicted by code trace: it means offloaded layers
Vulkan compute path instability | Load completes; crash occurs after runner start in compute stack | MATCH
Why gfx900 Still Works Sometimes
ROCm 7.2 excludes gfx900 from official support, but changelog says "no longer built by default" rather than "forbidden."
In the local ROCm install, gfx900 hsaco artifacts and `libggml-hip.so` strings were still present.
Interpretation:
unsupported means unguaranteed and untested, not necessarily impossible to execute.
This explains why ROCm/HIP can run while Vulkan still fails on the same Vega card.
7
Takeaway & Key Messages
✅
Support Status ≠ Execution Reality
Official exclusion does not imply absolute impossibility. Residual code paths, build targets, and shipped artifacts can still make gfx900 partially executable.
💡
Backend Choice Dominates Stability
On the same Vega/gfx900 device and the same model, ROCm/HIP passed fixed tests that Vulkan failed once GPU offload was enabled.
🔬
Reproducibility Before Claims
Gate matrices, code tracing, and matched work logs are necessary before declaring a legacy GPU "dead" or claiming a backend is stable.
Unsupported ≠ Impossible. | Legacy ≠ Poor. | Backend choice matters.